## Slide 1
Moinuddin Qureshi (moin@gatech.edu)
Moving the Needle in Rowhammer Defense with a Minimalist Approach
Keynote, DRAMSec-2025

## Slide 2
Painting vs. Sculpture?
A painting is complete when nothing more needs to be added
A sculpture is complete when nothing more can be removed

## Slide 3: The Rowhammer Saga
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 4: Rowhammer Attacks
Bit-Flips in Neighboring Rows
Row
Row
Row
Row of Cells (8KB)
Victim Row
Aggressor Row
Aggressor Row
DRAM
Rowhammer Attack
Rapid
Accesses
DRAM Scaling for Increased Capacity
More Inter-Cell Interference
DRAM
(old)
DRAM
(new)
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 5: Rowhammer Attacks
Bit-Flips in Neighboring Rows
Row
Row
Row
Row of Cells (8KB)
Victim Row
Aggressor Row
Aggressor Row
DRAM
Rowhammer Attack
Rapid
Accesses
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Software Adversary Can Flip Bits in Page Tables &
Gain Kernel Privileges (Take Over a System)
[Seaborn+, Blackhat’15]
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 6: Rowhammer is Getting Worse!
Rowhammer Threshold: TRH-S (Single Sided) and TRH-D (Double-Sided)
Solutions must tolerate not only current TRH but future TRH
30x Reduction in TRH in 8 years!
Notes: - With DRAM Scaling for increased capacity, DRAM cells are so close that activity on cells in one DRAM row causes charge leakage from cells in neighboring rows.
Rowhammer attacks exploit this phenomenon by accessing a DRAM row rapidly in a short window of time, that ends up causing bit-flips in neighboring rows. Essentially, this allows an adversarial software to flip bits in memory without accessing them.
Adversarial software can gain kernel-level privileges, by tampering the page-tables [Orig], or sensitive binaries like the sudo binary [Another-Flip], and even infer data in neighboring rows based on whether they flip or not [RamBleed].

## Slide 7: Typical Mitigation for Rowhammer
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
Tracking can be done at Memory Controller (MC) or In-DRAM
(In-DRAM mitigation can solve DRAM problem within DRAM)

## Slide 8: What is In-DRAM Mitigation?
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
In-DRAM Mitigation needs Space (Tracking) and Time (Victim Refresh)
DDR4: 4-16 Entries
Borrow Time from REF

## Slide 9: Refresh 101
In-DRAM borrows time from “REF” to perform RH mitigation
~73 ACTs
REF
Refresh 8-16
DRAM Rows
Check Tracker, Do
RH Mitigation

## Slide 10: What About the In-DRAM Tracker?
Optimal trackers incur high SRAM overheads. Low-Cost Trackers Secure?
Optimal Trackers
ProTRR, Mithril
(100-1000s entries)
Low-Cost Tracker
4-20 entries
(TRR, DSAC, PAT)

## Slide 11
Track Aggressor Rows
1
Mitigative Action
2
Victim Row
Aggressor Row
Victim Row
DRAM
Refresh
TRResspass Breaks TRR Tracker [Frigo+, SP’20]
Source: The Hacker News
Blacksmith Attack: All DDR4 DRAM Vulnerable [Jattke+, SP’22]
Source: The Register
Low-Cost In-DRAM Trackers Broken!
Targeted Row Refresh (TRR) in DDR4 (2015)
DRAM Industry: Our TRR was broken, so ALL low-cost TRR will be broken

## Slide 12
DRAM Industry: Throw the Baby Out with the Bathwater
TRR
Right question: How do we design a low-cost TRR that is provably secure?

## Slide 13
Outline
The Rowhammer Saga
MINT: Minimalist Randomized Tracker
MOAT: Secure Mitigation with PRAC
MoPAC: Reducing the Slowdown of PRAC
Parting Thoughts
MICRO-2024

## Slide 14: Why In-DRAM Trackers Fail?
In-DRAM Tracker
(Counters)
Insertion
Policy
Eviction Policy
Mitigation
Policy
In-DRAM Trackers characterized as having N entries and managed by 3 policies
Three sources of failures:
Insertion Failure (target address not get inserted in tracker within TRH)
Retention Failure (the address was inserted but got evicted without mitigation)
Tardiness (more activations between insertion and mitigation breaching TRH)
Build trackers such that it is easy to reason about the worst-case patterns and the resulting tolerated threshold

## Slide 15: The Problem of Non-Uniform Mitigation
The non-uniform mitigation means attacker can focus on most vulnerable position
Observation: In-DRAM PARA (IID Tracking) has non-uniform mitigation

## Slide 16: MINT: Minimalist In-DRAM Tracker
MINT requires low hardware overhead (about 4 bytes)
REF
REF
Window (can perform up to 73 ACT)
Which Row to Mitigate?
X = URAND (0,72) … LFSR
SAN=2
CAN=0
CAN=1
CAN=2
CAN=3
SAR
SAN: Selected Activation Num
CAN: Current Activation Num
SAR: Sampled Address Reg

## Slide 17: Deriving Worst-Case Pattern
What if we keep have 73 attack lines in the tREFI window? Failure probability becomes 73x
ABCDEF
MINT has a TRH of 2800, TRH-D of 1400 (25% lower than PrIDE)
Outperforming 700-entry tracker with a single-entry!
ABCDEF
ABCDEF
ABCDEF

## Slide 18: Refresh Postponement Attacks
Refresh postponement breaks low-cost trackers
Severity: Attacker can cause 478K unmitigated ACTs on a row!
(easy to tolerate with counter-based optimal trackers)

## Slide 19: Delayed Mitigation Queue (DMQ)
MINT+DMQ can tolerate a TRHD of 1482 (under Adaptive Attacks)
(within 2x of an idealized per-row tracker)
Simple Solution to Refresh Postponement Attacks
MINT+DMQ: 1 Mitig per tREFI
TRH-D: 1480, Slowdown=0%
MINT+DMQ+RFM16
TRH-D: 356, Slowdown=1.6%

## Slide 20: Row-Press: New Data-Disturbance Error
After ACT, neighbor row continue to leak charge on the bit line
Row-Press: Keep the row open for a long time!
Row-Press cause bitflips with fewer ACTs, breaks all RH trackers
[Luo, Mutlu, et al. ISCA-2023]

## Slide 21: Insight
Tolerate Row-Press without affecting tolerated threshold
No artificial limit on tON (applicable to in-DRAM trackers)
Only minor impact on storage and performance overheads
MICRO-2024

## Slide 22: Tolerating Row-Press with MINT?
MINT+ImPress defends both RH and RP at ultra-low cost!
Instead of incrementing CAN by 1 on ACT, increment by EACT
Select Row if CAN crosses SAN
REF
REF
Window (can perform up to 73 ACT)
Which Row to Mitigate?
X = URAND (0,72) … LFSR
SAN=2
CAN=0
CAN=1.5
CAN=2.8
CAN=4
SAR
SAN: Selected Activation Num
CAN: Current Activation Num
SAR: Sampled Address Reg

## Slide 23
Outline
The Rowhammer Saga
MINT: Minimalist Randomized Tracker
MOAT: Secure Mitigation with PRAC
MoPAC: Reducing the Slowdown of PRAC
Parting Thoughts
ASPLOS-25

## Slide 24: JEDEC Introduces PRAC+ABO
PRAC+ABO is a principled defense against RH (big changes to DRAM)
JEDEC: low-cost trackers broken, so let’s go for per-row tracking (space) and ABO (time)
PRAC: Per-Row-Activation-Counting, solves the space issue
ABO: Alert Back-off, solves the time issue

## Slide 25: Panopticon Design
Panopticon: seminal work & inspiration behind PRAC and ABO
PRAC is a framework, does not specify implementation details, security depends on design
Typically, some SRAM needed to track which row(s) will get mitigated
(8 entry queue per-bank)
One aggressor-row mitigated every Nth REF
Trigger ALERT if queue is full
Insert row in queue if threshold bit flips

## Slide 26: Exploiting Tardiness for Attack
Jailbreak inflicts 1150 ACTs on a row for design with threshold of 128
E.g. Design does not track activations while the row is buffered in the queue
We can attack this design by filling the queue, and hammering the youngest row

## Slide 27: MOAT: Minimalist Provably Secure Design
Insight: Greedily track a single entry per bank (minimalist design, low SRAM cost)
ATH: ALERT Threshold determines TRH
Row Addr
Ctr
CTA: Currently Tracked Addr
PRAC.Ctr > CTA.Ctr?
On Access
Yes
Overwrite
CTA
On ALERT/Mitigative REF: mitigate CTA
On Access: if CTA.Ctr > ATH, trigger ALERT
MOAT is the first provably secure implementation for PRAC+ABO

## Slide 28: MOAT Overheads (norm. to PRAC)
MOAT with ATH = 128+ incurs virtually zero ALERTs
The mitigation (ALERTs) from MOAT cause negligible performance overheads

## Slide 29
Outline
The Rowhammer Saga
MINT: Minimalist Randomized Tracker
MOAT: Secure Mitigation with PRAC
MoPAC: Reducing the Slowdown of PRAC
Parting Thoughts
ISCA-2025

## Slide 30: The Problem with PRAC
For row conflict, service time increases from 40ns to 62ns (1.5x)
For closed-page systems, tRC increase still significant (13%)
Two sources of slowdown: Intrinsic (inflated timing) + extrinsic (ABO related stalls)
PRAC suffers from high slowdown because of increased tRP/tRC (average 10% slowdown)

## Slide 31: The Problem with PRAC
Note: some prior studies showed 1% bus BW impact (BW != IPC)
The high tRP and tRC causes significant slowdown (consistent with other studies)
If PRAC related slowdown is high, will the industry adopt PRAC?

## Slide 32: Insight: Are all counter updates necessary?
MOPAC uses REF for ctr updates (triggers ABO if buffer fills up)
Instead of incrementing PRAC counter on each activation, update probabilistically
Revise ATH to account for sampling rate and sampling inefficiency

## Slide 33: Performance Overhead with MoPAC
MoPAC reduces the PRAC slowdown from 10% to 0.1%-2.2%
Unlike PRAC, MoPAC performance overhead depends on threshold

## Slide 34
Outline
The Rowhammer Saga
MINT: Minimalist Randomized Tracker
MOAT: Secure Mitigation with PRAC
MoPAC: Reducing the Slowdown of PRAC
DREAM: MC-Side Mitigations with DRFM
Parting Thoughts
ISCA-2025

## Slide 35: MC-Side Rowhammer Mitigation
MC-based RH mitigation enables SOC vendors to ensure security
Memory Controller
ACT
Mitigate
TRHD | p
500 | 1/25
1000 | 1/50
2000 | 1/100
Avoid obscure/proprietary DRAM TRR
Avoid slowdown of PRAC
Avoid reliance on REF cannibalization
Ensure security at low-cost in SOC
Why?

## Slide 36: DRFM: DDR5 Support for Mitigation
DRFM stalls 8-32 banks for each mitigation, performance impact?

## Slide 37: Slowdown from PARA with DRFM
Replacing NRR with DRFM causes significant slowdowns!

## Slide 38: Insight: Delay Issuing DRFM
Delaying gives other banks chance to sample into DAR
Delay until the next the next sampled row to the same bank
BANK 1
Pre+S
BANK 2
Pre+S
BANK 3
Pre+S
BANK 1
BANK 2
BANK 3
Concurrent Mitigation
How long should we delay?

## Slide 39: DRFM Aware Mitigation (DREAM)
MC-Side mitigation are quite useful (vs PRAC) for SOC vendors
DREAM has much lower slowdown than PRAC at current TRH

## Slide 40
Outline
The Rowhammer Saga
MINT: Minimalist Randomized Tracker
MOAT: Secure Mitigation with PRAC
MoPAC: Reducing the Slowdown of PRAC
DREAM: MC-Side Mitigations with DRFM
Parting Thoughts

## Slide 41
Painting vs. Sculpture

## Slide 42
Conclusion
Even after a decade, DRAM industry is unable to solve Rowhammer
Don’t throw TRR away – it is the lowest cost solution. Make it secure.
PRAC still needs to be carefully architected to ensure security
PRAC has high slowdown, need to reduce it for practical adoption
SOC vendors can take matters in their hand with DRFM, still useful for DDR6
Minimalism is key to ensuring security!
Performance matters: Everyone wants security, no one wants to pay